Exact solutions of laminar-boundary-layer equations
Taken from J.P. Holman, Heat Transfer, 6th edition, p. 653 ff.
We are looking at the laminar-boundary-layer over a flat plate, given by u(x,y) the fluid velocity in direction of x (parallel to the plate), v(x,y) the fluid velocity in direction of y (vertical to the plate) and T(x,y) the temperature. %%ii FUNCTION {{none},u,x;y} %%ii FUNCTION {{none},v,x;y} %%ii FUNCTION {{none},T,x;y}
The momentum and energy equations, assuming constant fluid properties, zero pressure gradient and no viscous-dissipation of the energy, are:
Continuity:	%%ii @B-1@ EQDEF differentiate(u, x, 1) + differentiate(v,y,1) = 0 {{alignc nospace{partial u}} over {alignc nospace{partial x}}} + {{alignc nospace{partial v}} over {alignc nospace{partial y}}} = 0 %%gg	(B-1), see also (5-12)
Momemtum:	%%ii @B-2@ EQDEF u differentiate(u,x,1) + v differentiate(u,y,1) = %ny differentiate( u,y,2 ) v {{alignc nospace{partial u}} over {alignc nospace{partial y}}} + u {{alignc nospace{partial u}} over {alignc nospace{partial x}}} = %nu {{alignc nospace{partial^{2}u}} over {alignc nospace{partial y^{2}}}} %%gg	(B-2), see also (5-13)
Energy:	%%ii @B-3@ EQDEF u differentiate(T,x,1) + v differentiate(T,y,1) = %alpha differentiate( T,y,2 ) u {{alignc nospace{partial T}} over {alignc nospace{partial x}}} + v {{alignc nospace{partial T}} over {alignc nospace{partial y}}} = %alpha {{alignc nospace{partial^{2}T}} over {alignc nospace{partial y^{2}}}} %%gg	(B-3), see also (5-22)
Here ν is the kinematic viscosity of the fluid and α the thermal diffusivity defined as:
%%ii @1@ EQDEF %alpha = k over { %rho c_p} %alpha = k over { %rho c_p} %%gg
where k is the thermal conductivity, ρ the density and cp the specific heat at constant pressure.
From an order-of-magnitude analysis we have the relation
%%ii @B-4@ EQDEF %delta = hat %eta sqrt{{%ny x} over u_infinity} %delta = hat %eta sqrt{{%nu x} over u_infinity} %%gg	(B-4)
where δ is the boundary layer thickness and η̂ is some proportionality constant.
We now assume that the velocity profiles have similar shapes at various distances from the leading edge of the flat plate. Then the ratio of the velocity u at a certain distance x to the final velocity u∞ can be expressed as a function g( η(x,y) ): %%ii FUNCTION {{none},%eta,x;y} %%ii FUNCTION {{none},g,%eta}
%%ii @2@ {autoformat=true} EQDEF u over u_infinity = g left( y over %delta right) %%ii {autoformat=true} TEXT newline %%ii @3@ {autoformat=true} EQDEF SUBSTC(@2@, @B-4@) MATRIX { %%gg {alignr {{alignc u } over {alignc u_infinity }}}#{}={}# {alignl g({{alignc y} over {alignc %delta}})} ## %%gg {} #{}={}# {alignl g({{alignc y } over {alignc {hat %eta} sqrt{size-1{{alignc x %nu } over {alignc u_infinity}}} }})} %%gg } %%gg
Introducing the similarity variable η(x,y) and choosing %%ii @hateta@ EQDEF hat %eta = 1 hat %eta = 1 %%gg , the function we are looking for is
%%ii @B-6@ EQDEF* %eta = y sqrt{u_infinity over {x %ny}} %%gg %%ii @B-5@ {autoformat=true} EQDEF SUBSTC(SIMPLIFY(SUBST(@3@, SOLVE(@B-6@, y, 1)) , "unsafe"), @hateta@) {{alignc u } over {alignc u_infinity }} = g(%eta) %%gg	(B-5)
with %%ii @5@ EQDEF @B-6@ %eta = y sqrt{{{alignc u_infinity} over {alignc x %nu }}} %%gg .	(B-6)
We now define a stream function ψ(x,y) so that %%ii FUNCTION {{none},%psi,x;y}
%%ii @B-7@ EQDEF u = differentiate( %psi,y,1 ) u = {{alignc nospace{partial %psi}} over {alignc nospace{partial y}}} %%gg	(B-7)
%%ii @B-8@ EQDEF v =- differentiate( %psi,x,1 ) v = -{{alignc nospace{partial %psi}} over {alignc nospace{partial x}}} %%gg	(B-8)
This function fulfills the continuity equation (B-1).
Inserting this stream function in (B-5) gives
%%ii @6@ EQDEF SUBST(@B-5@, @B-7@) {{alignc 1 } over {alignc u_infinity }} {{alignc nospace{partial %psi}} over {alignc nospace{partial y}}} = g(%eta) %%gg → %%ii @7@ EQDEF* SIMPLIFY(@6@ * (u_infinity partial(y)), "cancel-diff") %%gg %%ii @8@ {autoformat=true} EQDEF* SUBSTC(@7@, partial(%psi) = differential(%psi); partial(y) = differential(y)) %%gg %%ii @9@ {autoformat=true} EQDEF SUBSTC(SIMPLIFY(INT{LHS(@prev@)} = INT{RHS(@prev@)} , "integrate"), C=0) %psi = u_infinity int {g(%eta)} nospace{dy} %%gg
and after substituting (from B-4) %%ii @dy@ {autoformat=true} EQDEF SIMPLIFY(SOLVE(SIMPLIFY(DIFFERENTIATE(@B-6@, y, 1) * partial( y ) , "cancel-diff"), partial(y), 1) , "normal") nospace{partial y} = sqrt{{{alignc x %nu } over {alignc u_infinity}}} nospace{partial %eta} %%gg and defining %%ii FUNCTION {{none},f,%eta} %%ii @f_eta@ EQDEF f(%eta) = int { g(%eta) differential(%eta)} f(%eta) = int {g(%eta)} nospace{d%eta} %%gg
%%ii @10@ EQDEF SUBST(@9@, @dy@) %psi = u_infinity int {sqrt{{{alignc x %nu } over {alignc u_infinity}}} g(%eta) } nospace{d%eta} %%gg %%ii @12@ EQDEF* SIMPLIFY(@10@ , "integrate") %%gg	(B-9)
%%ii @13@ EQDEF SUBSTC(@12@, REV(@f_eta@)) %psi = u_infinity sqrt{{{alignc x %nu } over {alignc u_infinity}}} f(%eta) %%gg
The partial derivatives of η are:
%%ii @15@ {autoformat=true} EQDEF SIMPLIFY(DIFFERENTIATE(@5@, x, 1) , "normal") {{alignc nospace{partial %eta}} over {alignc nospace{partial x}}} = -{{alignc 1} over {alignc 2}} {{alignc u_infinity y sqrt{size-1{{alignc x %nu } over {alignc u_infinity}}} } over {alignc %nu x^{2} }} %%gg → %%ii @deta_dx@ {autoformat=true} EQDEF SIMPLIFY(SUBSTC(@15@, SOLVE(@B-6@, y , 1)) , "normal") {{alignc nospace{partial %eta}} over {alignc nospace{partial x}}} = -{{alignc 1} over {alignc 2}} {{alignc %eta } over {alignc x }} %%gg ,
%%ii @deta_dy@ {autoformat=true} EQDEF DIFFERENTIATE(@5@, y, 1) {{alignc nospace{partial %eta}} over {alignc nospace{partial y}}} = sqrt{{{alignc u_infinity} over {alignc x %nu }}} %%gg and
%%ii @d2eta_dy2@ {autoformat=true} EQDEF DIFFERENTIATE(@5@, y, 2) {{alignc nospace{partial^{2}%eta}} over {alignc nospace{partial y^{2}}}} = 0 %%gg
Differentiating ψ and substituting the partial derivative of η, we find that
%%ii @14@ {autoformat=true} EQDEF SIMPLIFY(DIFFERENTIATE(@13@, x, 1) , "unsafe";"collect-common";"gather-sqrt") %%ii TEXT newline %%ii @16@ {autoformat=true} EQDEF SIMPLIFY(SUBSTC(@14@, @deta_dx@) , "collect-common";"gather-sqrt") MATRIX { %%gg {alignr {{alignc nospace{partial %psi}} over {alignc nospace{partial x}}}}#{}={}# {alignl {{alignc 1} over {alignc 2}} sqrt{u_infinity %nu } ({{alignc f(%eta) } over {alignc sqrt{x} }} + 2 sqrt{x} {{alignc d{f(%eta)}} over {alignc nospace{d%eta}}} {{alignc nospace{partial %eta}} over {alignc nospace{partial x}}} ) } ## %%gg {} #{}={}# {alignl {{alignc 1} over {alignc 2}} sqrt{{{alignc u_infinity %nu } over {alignc x}}} (f(%eta)-%eta {{alignc d{f(%eta)}} over {alignc nospace{d%eta}}} ) } %%gg } %%gg
Using this in (B-8) gives
%%ii @B-10@ {autoformat=true} EQDEF SUBST(@B-8@, @prev@) v = {{alignc 1} over {alignc 2}} sqrt{{{alignc u_infinity %nu } over {alignc x}}} (%eta {{alignc d{f(%eta)}} over {alignc nospace{d%eta}}} -f(%eta) ) %%gg	(B-10)
Now we transform (B-2) using %%ii @u_eta@ EQDEF SOLVE(@B-5@, u, 1) u = u_infinity g(%eta) %%gg from (B-5). The partial derivatives of u are:
%%ii @20@ EQDEF DIFFERENTIATE(@u_eta@, x, 1) {{alignc nospace{partial u}} over {alignc nospace{partial x}}} = u_infinity {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} {{alignc nospace{partial %eta}} over {alignc nospace{partial x}}} %%gg → %%ii @du_dx1@ EQDEF SUBSTC(@20@, @deta_dx@) {{alignc nospace{partial u}} over {alignc nospace{partial x}}} = -{{alignc 1} over {alignc 2}} {{alignc u_infinity %eta } over {alignc x }} {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} %%gg
%%ii @19@ EQDEF DIFFERENTIATE(@u_eta@, y, 1) {{alignc nospace{partial u}} over {alignc nospace{partial y}}} = u_infinity {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} {{alignc nospace{partial %eta}} over {alignc nospace{partial y}}} %%gg → %%ii @du_dy1@ EQDEF SUBSTC(@19@, @deta_dy@) {{alignc nospace{partial u}} over {alignc nospace{partial y}}} = u_infinity sqrt{{{alignc u_infinity} over {alignc x %nu }}} {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} %%gg
%%ii @38@ EQDEF DIFFERENTIATE(@u_eta@, y, 2) {{alignc nospace{partial^{2}u}} over {alignc nospace{partial y^{2}}}} = u_infinity ({{alignc nospace{partial %eta}} over {alignc nospace{partial y}}})^{2} {{alignc d^{2}{g(%eta)}} over {alignc nospace{d%eta^{2}}}} + u_infinity {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} {{alignc nospace{partial^{2}%eta}} over {alignc nospace{partial y^{2}}}} %%gg → %%ii @d2u_dy2@ EQDEF SUBSTC(@38@, @deta_dy@;@d2eta_dy2@) {{alignc nospace{partial^{2}u}} over {alignc nospace{partial y^{2}}}} = {{alignc u_infinity^{2}} over {alignc x %nu }} {{alignc d^{2}{g(%eta)}} over {alignc nospace{d%eta^{2}}}} %%gg
Substituting these derivatives, u from (B-5) and v from (B-10) gives:
%%ii @26@ EQDEF SUBSTC(@B-2@, @du_dy1@;@du_dx1@;@d2u_dy2@) u_infinity sqrt{{{alignc u_infinity} over {alignc x %nu }}} v {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} -{{alignc 1} over {alignc 2}} {{alignc u_infinity %eta u } over {alignc x }} {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} = {{alignc u_infinity^{2}} over {alignc x}} {{alignc d^{2}{g(%eta)}} over {alignc nospace{d%eta^{2}}}} %%gg
%%ii @39@ EQDEF SUBSTC(@26@, @u_eta@;@B-10@) -{{alignc 1} over {alignc 2}} {{alignc u_infinity^{2} %eta g(%eta) } over {alignc x }} {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} + {{alignc 1} over {alignc 2}} u_infinity sqrt{{{alignc u_infinity} over {alignc x %nu }}} sqrt{{{alignc u_infinity %nu } over {alignc x}}} (%eta {{alignc d{f(%eta)}} over {alignc nospace{d%eta}}} -f(%eta) ) {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} = {{alignc u_infinity^{2}} over {alignc x}} {{alignc d^{2}{g(%eta)}} over {alignc nospace{d%eta^{2}}}} %%gg
Since %%ii @df_deta@ EQDEF differentiate(f(%eta), %eta, 1) = g(%eta) {{alignc d{f(%eta)}} over {alignc nospace{d%eta}}} = g(%eta) %%gg , we can use %%ii @d2f_deta2@ EQDEF DIFFERENTIATE(@df_deta@, %eta, 1) {{alignc d^{2}{f(%eta)}} over {alignc nospace{d%eta^{2}}}} = {{alignc d{g(%eta)}} over {alignc nospace{d%eta}}} %%gg and %%ii @d3f_deta3@ EQDEF DIFFERENTIATE(@d2f_deta2@, %eta, 1) {{alignc d^{3}{f(%eta)}} over {alignc nospace{d%eta^{3}}}} = {{alignc d^{2}{g(%eta)}} over {alignc nospace{d%eta^{2}}}} %%gg to obtain an ordinary differential equation in f(η):
%%ii @41@ EQDEF SUBSTC(@39@, REV(@d3f_deta3@);REV(@d2f_deta2@);REV(@df_deta@)) -{{alignc 1} over {alignc 2}} {{alignc u_infinity^{2} %eta } over {alignc x }} {{alignc d^{2}{f(%eta)}} over {alignc nospace{d%eta^{2}}}}{{alignc d{f(%eta)}} over {alignc nospace{d%eta}}} + {{alignc 1} over {alignc 2}} u_infinity sqrt{{{alignc u_infinity} over {alignc x %nu }}} sqrt{{{alignc u_infinity %nu } over {alignc x}}} (%eta {{alignc d{f(%eta)}} over {alignc nospace{d%eta}}} -f(%eta) ) {{alignc d^{2}{f(%eta)}} over {alignc nospace{d%eta^{2}}}} = {{alignc u_infinity^{2}} over {alignc x}} {{alignc d^{3}{f(%eta)}} over {alignc nospace{d%eta^{3}}}} %%gg %%ii @43@ EQDEF SIMPLIFY(@41@ , "expandf") -{{alignc 1} over {alignc 2}} {{alignc u_infinity^{2} f(%eta) } over {alignc x }} {{alignc d^{2}{f(%eta)}} over {alignc nospace{d%eta^{2}}}} = {{alignc u_infinity^{2}} over {alignc x}} {{alignc d^{3}{f(%eta)}} over {alignc nospace{d%eta^{3}}}} %%gg
%%ii @44@ {autoformat=true} EQDEF SIMPLIFY(@43@ * (x / u_infinity^2) , "expand") -{{alignc 1} over {alignc 2}} f(%eta) {{alignc d^{2}{f(%eta)}} over {alignc nospace{d%eta^{2}}}} = {{alignc d^{3}{f(%eta)}} over {alignc nospace{d%eta^{3}}}} %%gg
%%ii @46@ {autoformat=true} EQDEF (@44@ - (RHS(@prev@))) * (-2) f(%eta) {{alignc d^{2}{f(%eta)}} over {alignc nospace{d%eta^{2}}}} + 2 {{alignc d^{3}{f(%eta)}} over {alignc nospace{d%eta^{3}}}} = 0 %%gg
This equation can be solved numerically for f(η).